## Slide 1
INDICATIONS:
Urgent/emergency RRT may be indicated for conditions refractory to medical therapy:
· A: Acidosis (usually severe metabolic)
· E: Electrolyte derangements (hyperkalemia, hypercalcemia, etc)
· I: Intoxications (APAP, Barbiturates, Lithium, carbamazepine, metformin, methanol, salicylates, thallium, theophylline, valproate, etc); see ExTRIP guidelines
· O: Fluid Overload (pulmonary edema refractory to diuretics, uncontrolled hypertension, etc). Volume removal may also hasten liberation from ventilation.
· U: Symptomatic Uremia (causing severe altered mental status, uremic pericarditis, bleeding diathesis, etc)
renal replacement therapy
onepagericu.com
@nickmmark
Link to the most current version →
ONE
DEFINITION:
Renal Replacement Therapies (RRT) are used in patients in the IUC with renal failure to remove excess fluid or to clear the blood of toxins (such as urea or potassium).
· Clearance (K) is the volume of blood cleared of a solute (typically urea) per time. Clearance depends on Blood flow (QB), dialysate flow (QD) and the dialyzer. There are two primary mechanisms involved:
· Diffusion (with dialysis) clears smaller molecules (<200 D), while convection (with UF) clears small & medium sized (< 50kD) molecules.
by Nick Mark MD
MODALITIES OF RRT IN THE ICU:
COMPONENTS OF A HEMODIALYSIS CIRCUIT & PARAMETERS SET:
AV fistula
Tunneled central venous dialysis catheter
Temporary central venous dialysis catheter
dialysate flow QD
blood flow QB
replacement fluid
dialysate
effluent
Anticoagulant
(citrate or heparin)
Blood
Pump
“Arterial” or access pressure
Filter pressure
“Venous” or return pressure
BLOOD FLOW RATE (QB) is the flow rate of blood through the dialysis circuit. Higher flows enable greater clearance/UF & have lower thrombosis risk but may require larger access & have more adverse hemodynamic effects.
ULTRAFILTRATION (UF) is the filtration of water from the blood, driven by the transmembrane pressure (TMP) gradient between the blood & effluent. TMP can be titrated by adjusting the effluent pump & pressure.
Ultrafiltration (UF) provides clearance by convection (also called solute drag) removing small & medium sized molecules.
Dialysate pressure
Effluent
Pump
Dialysate
Pump
Effluent pressure
DIALYZER is rigid case that encloses thousands of semi-permeable polymer tubules. Blood flows through the tubules & dialysate flows in the opposite direction outside (countercurrent). Dialyzers differ in surface area, hydraulic permeability (KUF), permeability to medium sized molecules (flux of β2 microglobulin), & permeability to small molecules diffusion (mass transfer coefficient)
DIALYSATE FLOW RATE (QD)
is a countercurrent flow of dialysate through the dialyzer. Higher flow rates enable greater clearance of small molecules via diffusion.
DIALYSATE SOLUTION is an isotonic fluid containing electrolytes, bicarbonate/acetate, glucose, & sometimes other small molecules. The dialysate is chosen to match serum osmolality & to correct any blood chemistry abnormalities; e.g:
REPLACEMENT FLUID (RF) can be used to restore fluid volume removed by UF in the dialyzer. Replacement fluid can be given pre- or post-dialyzer.
VASCULAR ACCESS can be permanent (such as an AV fistula or an AV graft) accessed using needles, semi-permanent (a tunneled CVC), or temporary (such as a non-tunneled CVC). NB: The “arterial” (red) side describes blood coming out of the patient; it does NOT mean that it comes out of an artery.
Anticoagulant reversal
ANTICOAGULATION may be used to reduce thrombosis in the circuit. It is typically reversed on return.
 | IHD (Intermittent HD) | SLEDD (Sustained low efficiency daily dialysis) | CRRT (Continuous renal replacement therapy)
Description | 3-5 hr session using standard HD machine | ~12 hr session using standard HD machine | 24 hr (continuous) session using a CRRT machine
Logistics | Typically done by dialysis RNs Requires fresh water & drain connections |  | Typically done by CCRNs Uses sterile fluid bags
Vascular Access | Fistula/Graft or CVC | Usually requires CVC | Requires CVC
QB / QD | > 300 ml/min > 500 ml/min | ~ 200 ml/min 100-200 ml/min | < 200 ml/min <50 ml/min (depends on mode)
Clearance | Highest; ideal for hyperK or toxins | Moderate | Low; ideal for slower correction of abnormalities & fluid removal
Hemodynamics | Hypotension common | Causes less hypotension | Causes the least hypotension
Other risks | Risk of disequilibrium syndrome | Risk of hypoPhos, unclear med pharmacokinetics | Thrombosis risk, immobility, higher cost
CRRT Mode | Description | Schematic
SCUF | Slow continuous UF; UF removes fluid but provides almost no clearance and does not correct pH; no replacement fluid required. Corrects volume overload only. | 
CVVH (a.k.a.CVVHF) | Continuous venovenous hemofiltration. Provides convective clearance by filtering a large volume of blood; Replacement fluid restores volume lost. Corrects uremia, lytes, pH and can remove volume. | 
CVVHD | Continuous venovenous hemodialysis. Provides diffusive clearance by running dialysate opposite blood flow. No replacement fluid used. Gently corrects uremia, lytes, pH | 
CVVHDF | Continuous venovenous hemodiafiltration. High clearance achieved using both UF & dialysate flow (both convection & diffusion). Replacement fluid used. Allows fluid removal and correction of electrolyte/pH. Good for toxin removal. | 
UF
UF
RF
RF
Dialysate
Dialysate
UF
Bubble detector
Heater warms returning blood
CC BY-SA 3.0 v1.0 (2021-02-17)
DIALYZER